## Slide 1: Sensor Networks Lab: Introduction
Daniel van den Akker
Notes: 1

## Slide 2: Introduction

## Slide 3: Introduction
Sensor Network:
“A sensor network is composed of a large number of sensor nodes which are densely deployed either inside or very close to the phenomenon of interest”
Notes: Original idea: ‘smart dust’
-Not too feasible, but some nice applications have emerged
Example: forest monitoring

## Slide 4: Introduction
Sensor nodes
  ‘Small’, low power and low cost devices
  Consist of sensing, data processing and communication components
  Are used to sense the environment
    Eg: temperature, humidity, …
  Can sometimes be used to interact with the environment
    In that case it is called an actuator
http://theon.github.io/plant-watering-with-arduino.html
http://www.electronicsweekly.com/news/research/device-rd/isscc-rice-grain-solar-sensor-nodes-uses-cortex-m3-2010-02/

## Slide 5: Sensor network applications
Habitat & Agricultural monitoring
  Seabird monitoring in Maine’s Great Duck Island[1]
  Mesa Network (Climate monitoring)[2]
  SERVIR Flash flood detection system[3]
[1] http://www.wired.com/wired/archive/11.12/network.html
[2] https://intelesense.net/customers/uidaho
[3] https://servirglobal.net/Himalaya/Articles/tabid/243/Article/1217/servirs-wireless-sensor-network-wsn-flash-flood-early-warning-system-deployed-i.aspx

## Slide 6: Sensor network applications
Structural and seismic monitoring
  Bridges
  Highways
  Buildings
  Examples
    Structural Health Monitoring of the Golden gate bridge[1]
    UCLA Factor building[2]
[1] http://www.cs.berkeley.edu/~binetude/ggb/
[2] http://factor.gps.caltech.edu/node/61

## Slide 7: Sensor network applications
Home & Building Automation

## Slide 8: Sensor network applications
Surveillance
  Perimeter control
  Reconnaissance
Logistics
  Trace & Tracking of containers
Smart Environments
  Manufacturing
  Smart Roads
  …
http://www.libelium.com/wireless_sensor_networks_m2m_logistics_operations/
http://defense-update.com/20060107_scout-ugs.html

## Slide 9: Sensor network properties
Limited energy sources
  Battery powered nodes
    Infeasible to replace
    Difficult to charge: solar panels, wind, …
  Tradeoff between performance and energy usage / lifetime
    Nodes are expected to last for years
One-time Ad-hoc deployment
  Single or (Limited) Multihop wireless network
    Little to no infrastructure available
  Self organising & self healing
    Limited control over node placement
    Post-deployment intervention is difficult or impossible

## Slide 10: Sensor network properties
Varying network topologies
  Between 10s and 1000s of nodes
  Varying density levels
  Both static & mobile nodes
    Eg: shipping containers being moved
Limited data rates
  Periodical reporting of sensor data
    Every few minutes to a few times a day
    Eg: average temperature & humidity
  Occasional traffic bursts
    In response to events sensed by the nodes
    Eg: temperature indicates a fire

## Slide 11: Sensor  Ad-hoc Networks
 | Sensor Network | Ad-hoc Network
Type | Self organising, Multihop wireless network | 
Scale | 100+ Nodes | 10-50 Nodes
Memory | 8K – 512K RAM | 1G – 4G RAM
Processing power | 4MHz – 128MHz Microcontroller | ± 1Ghz CPU
Price | Cheap: less than 5€ per node | Relatively expensive: 100 – 200€ per node
Typical energy usage | 0.1mW – 100mW | 5-25W
Dependability | Nodes are prone to failure, network is more important | Node failure should be avoided
Application support | Single Application | Multiple Applications

## Slide 12: Energy Usage
Which metric should be optimised ?
  Energy per correctly received bit
    Including overheads, forwards by nodes, …
  Energy per reported (unique) event
    After all: the information is important, not the payload bits
    Typical for WSN
  Network lifetime: “Time until the network is no longer useful”
    Time to first node failure
    Time to partition
    Time to loss of coverage
    Time to failure of first event notification
    …

## Slide 13: Energy Usage
What is more expensive: computation or communication ?
  Difficult to compare directly
  : between 200 and 2900 (according to literature)
    To send one kilobyte ≈ computing three million instructions[1]
  Computation is generally preferable to communication
    In-network processing:
      Exploit compression/coding schemes, …
      Aggregation
    Tradeoffs:
      Eg: Energy  Accuracy
    Optimise the network stack
[1] Pottie, Gregory J., and William J. Kaiser. "Wireless integrated network sensors." Communications of the ACM 43.5 (2000): 51-58.

## Slide 14: Other design challenges
QoS constraints
  Delay, reliability, …
  Depends on the application
Heterogeneity
  Not all nodes may have the same capabilities
Adaptability
  Changing application requirements
  Changing operation conditions (eg: weather)
  …
Security & Privacy
  Sensor networks collect potentially sensitive information
  Are subject to attacks, just like other wireless networks

## Slide 15: Network Stack: Physical Layer

## Slide 16: Physical Layer
IEEE 802.15.4:
  Standard for low-power Wireless (Personal) Area Networks
  Frequency bands:
    433MHz, 780MHz, 868MHz, 915MHz, 950MHz
      Different bands available in different countries
      Data rates: 20 – 250kbit/sec
    ISM Band: 2.4GHz
      Available worldwide
      Data rates: 250 – 1000kbit/sec
    UWB
  Packet size: max 127 bytes
  Range: between 10m – +1km
    Depends on frequency band, modulation, obstacles, …
Notes: IEEE 802.15.4: eg used in philips hue lamps; lots of ‘remote controllable’ IKEA devices
Especially on 443 long ranges are possible: right data rate && right antenna: 1.5km not really an issue

## Slide 17: Physical Layer
IEEE 802.15.4  Wifi
  Overlapping channel allocation[1]:
  Different PHY Parameters:
[1] Liang, Chieh-Jan Mike, et al. "Surviving wi-fi interference in low power zigbee networks." Proceedings of the 8th ACM Conference on Embedded Networked Sensor Systems. ACM, 2010.
Parameters | IEEE 802.15.4 | IEEE 802.11b
Tx Power | 0 dBm (1mW) | 20 dBm (100mW)
Channel width | 2MHz | 22MHz
CCA Threshold | -75 dBm | -82 dBm

## Slide 18: Physical Layer
IEEE 802.15.4  WiFi
  IEEE 802.15.4 is severely affected by interference from WiFi networks[1]
  Mitigation strategies:
    Use a channel not used by any WiFi networks (if available)
    IEEE 802.15.4e: channel hopping
[1] Liang, Chieh-Jan Mike, et al. "Surviving wi-fi interference in low power zigbee networks." Proceedings of the 8th ACM Conference on Embedded Networked Sensor Systems. ACM, 2010.

## Slide 19: Physical Layer
Other Transmission technologies used
  UMTS/GSM
    Extremely low frequency data reporting in urban environments
  LoRa
    Extremely long range: Urban: 2km+, Rural: 10km+
    Extremely low bitrate: 300 bit/sec
    Requires proprietary radio chip
  SigFox
    Range: Urban: 3km+, Rural: 30km+
    Extremely low bitrate: 10 – 1000 bit/sec
    Sensors can use ‘default’ radio chips
    Basestations are proprietary
Notes: 300 bit/sec -> Takes 4 seconds just to transmit a twitter msg

## Slide 20: Network Stack: Medium Access Control (MAC) Layer

## Slide 21: MAC Layer
Energy efficiency:
  Primary Design goal: Minimise energy consumption
  Radio States
  Try to SLEEP as much as possible
    “Duty Cycle” = fraction of the time the radio is ‘active’
State | Description | Typical power drawn[1] | Time needed to switch to RX state[1]
OFF | Radio is completely disabled No RX / TX Possible Startup takes a significant amount of time | 0 mA | 5 – 10 ms
SLEEP | Some hardware functions disabled No RX / TX Possible Radio can quickly change to RX state | 0.426 mA | 0.192ms
RX | Radio is actively scanning for packets to receive | 18.8 mA | 0
TX | Radio is transmitting a packet | 8.5 – 17.4 mA | 0.192ms
[1] http://www.ti.com/product/cc2420

## Slide 22: MAC Layer
Sources of energy waste
  Idle Listening:
    Radio is in RX state while not receiving packets
  Overhearing
    Receiving packets destined to other nodes
      Keeps the CPU busy unnecessarily
      Prevents the CPU from entering its ‘low power’ mode
    Problematic for high network loads / high network density
  Collisions:
    Retransmissions prolong the ‘active’ time of the radio
  Control Traffic

## Slide 23: Other design goals
Scalability
  Sensor networks consist of 100+ nodes
  Varying density levels
Adaptability
  Mobile nodes, Channel conditions change over time
  Varying traffic patterns: Periodic reporting  Event triggered
Robustness
  Sensors fail all the time, MAC should be able to cope
Quality of Service
  Usually not too important as long as a minimum quality is achieved
    Eg: 95% loss is not acceptable under any circumstances
Notes: Depend on specific application; not all of them are important for each use case

## Slide 24: TDMA MAC protocols
Time Division Multiple Access (TDMA)
  Divide the channel into repeating (super-)frames
    Each frame consists of N slots
    Nodes are assigned specific slots for packet reception & transmission
    Easily combined with frequency hopping
  Very energy efficient
    Radio is only on when transmitting or receiving
      No idle listening, No overhearing
    Collision free
  Built-in QoS support
    TDMA Slot allocation can be calculated according to specific delay & throughput constraints

## Slide 25: TDMA MAC protocols
Time Division Multiple Access (TDMA)
  Difficult to apply to sensor networks
    TDMA Requires:
      Precise time synchronisation (0.25ms – 0.5ms)
      Nodes to agree on the slot allocation
    Simple for single-hop, difficult for (large-scale) multi-hop networks
    Nodes are resource constrained
  Limited scalability & adaptability
    Slot allocation changes when nodes join/leave
    Frame length is fixed, number of nodes can change over time

## Slide 26: TDMA MAC protocols
Cluster-based TDMA protocols
  Organise the network into different clusters
    A single cluster is effectively a single hop network
  “Clusterhead”: controls communication within the cluster
    Provides timing & TDMA slot allocation within the cluster
    Similar to a WiFi access point
  Inter-cluster communication:
    Use a different radio
    Hierarchical clustering
  Examples: LEACH, SS-TDMA

## Slide 27: TDMA MAC protocols
Multi-hop TDMA mechanisms
  Time Synchronisation
    Hierarchical: synchronise according to predefined tree
    Broadcast based:
      All nodes broadcast timing information
      Nodes adjust their clocks to minimise drift wrt. their neighbours
  Slot Allocation
    Centralised solutions:
      Slot assignment determined by central controller
    Distributed algorithms:
      Collision based reservation
      Distributed graph colouring
      …

## Slide 28: TDMA MAC Protocols
Further Reading
  W.B. Heinzelman, A.P. Chandrakasan and H. Balakrishnan. An application-specific protocol architecture for wireless microsensor networks. IEEE Transactions on Wireless Communications, 1(4):660–670, October 2002.
  Kulkarni, Sandeep S., and Mahesh Arumugam. "SS-TDMA: A self-stabilizing MAC for sensor networks." Sensor network operations (2006).
  Assegei, Fasika A. "Decentralized frame synchronization of a TDMA-based wireless sensor network." Master's Thesis, Eindhoven University of Technology, Department of Electrical Engineering (2008).
  Chen, Zhihui, and Ashfaq Khokhar. "Self organization and energy efficient TDMA MAC protocol by wake up for wireless sensor networks." Sensor and Ad Hoc Communications and Networks, 2004. IEEE SECON 2004. 2004 First Annual IEEE Communications Society Conference on. IEEE, 2004.
  Herman, Ted, and Sébastien Tixeuil. "A distributed TDMA slot assignment algorithm for wireless sensor networks." Algorithmic Aspects of Wireless Sensor Networks. Springer Berlin Heidelberg, 2004. 45-58.

## Slide 29: Contention-based MAC Protocols
Contention-based MAC Protocols
  Channel is shared amongst all nodes
  Nodes contend with each other for channel access
  Advantages
    Easier to implement
    Better Adaptability & Scalability
    More resilient to node failures
    Little to no time synchronisation required
  Disadvantages
    Less energy efficient: Idle listening, overhearing, collisions
    Bandwidth utilisation & QoS support not as good as TDMA

## Slide 30: Contention-based MAC Protocols
CSMA/CA
  Versatile and easy to implement
  Extremely wasteful of energy
    Radio must be kept on the entire time !
  Still used to this day
    Often in combination with power reduction schemes at higher layers
S-MAC
  One of the earliest “true” sensor network MAC protocols
  Combines CSMA/CA with a periodic listen/sleep cycle
  Collision & Overhearing avoidance

## Slide 31: Contention-based MAC Protocols: S-MAC
S-MAC
  Frame = one complete sleep cycle
    frameTime: total length of the frame
    activeTime: length of the listen interval
  Frames are not necessarily synchronised between nodes
  Packets are sent during the listen period of the receiver
activeTime
Node A:
Listen
Sleep
Sleep
Listen
Listen
Sleep
time
Node B:
Listen
Sleep
Listen
Listen
Sleep
Sleep
time
frameTime
Packet transmission

## Slide 32: Contention-based MAC Protocols: S-MAC
Sleep scheduling
  Each node
    Maintains a schedule table containing the sleep schedules of its neighbours
    Announces its own sleep schedule by broadcasting a ‘SYNC’ packet every few frames
    Periodically listens for an entire frame to discover new neighbours
  Nodes try to synchronise to a common sleep schedule
    At startup, nodes adopt the first schedule they hear
    If no schedule is received after a ‘random’ time, a new schedule is started
Notes: Synchronisation needed just like with TDMA but precision requirements are more ‘relaxed’

## Slide 33: Contention-based MAC Protocols: S-MAC
Schedule creation
  Synchroniser: First node to transmit a schedule
  Followers: Nodes adopting this schedule
    Re-broadcast the schedule after a random delay
    This allows more distant nodes to follow the schedule
  Multiple schedules may exist
    Synchronisation wave may not reach entire network in time
    Nodes adopt all schedules they hear but only broadcast their ‘primary’ schedule
Schedule 1
Schedule 1+2
Schedule 2
Notes: Q: why wait for a random delay ?
A:: to prevent ‘flooding’ at startup

## Slide 34: Contention-based MAC Protocols: S-MAC
Contention resolution in S-MAC:
  Same as in IEEE 802.11
  Broadcast: CSMA/CA only
  Unicast: also use RTS – CTS – DATA – ACK
    Nodes overhearing RTS/CTS go to sleep
      Reduces idle listening, overhearing
RTS – CTS overhead:
  RTS – CTS creates at least 41% overhead !!
SIFS
RTS
CTS
Data
ACK
19 bytes
19 bytes
max 127 bytes
5 bytes
1884µs
4512µs
time
Notes: Note: S-MAC was designed in the pre IEEE 802.15.4 era,
For radios supporting near ‘infinite’ packet lengths

## Slide 35: Contention-based MAC Protocols S-MAC
How to reduce RTS – CTS overhead ?
  Disable RTS – CTS: also done in IEEE 802.11 for smaller frames
  Buffer packets & send them in a burst: RTS – CTS is only performed once
Advantages
  Duty cycle can be tuned by setting frameTime & activeTime
  Single node failure does not affect other nodes
Disadvantages
  Limited scalability: neighbour tables grow with the network density
  S-MAC does NOT adapt to changing bandwidth requirements
    frameTime & activeTime are set during deployment
    Bandwith requirements are not the same in the entire network
    Bandwith requirements may change over time
  Successor: T-MAC ≈ S-MAC with traffic-adaptive listen period

## Slide 36: Low power listening MAC Protocols
Low power listening protocols
  Nodes periodically wake up and check for channel activity
    Activity detected  stay awake for a specific listenTime
    No activity detected  go back to sleep for a specific sleepTime
  Sending a packet
    prefix the packet with a ‘busy’ signal to wakeup the receiver
    The busy signal needs to be at least sleepTime long
Sender:
Receiver:
Busy signal
Data
Listen
Notes: Lots of different ways to generate a busy signal

## Slide 37: Low power listening MAC Protocols
May different low power listening MAC protocols exist
  B-MAC: The first of the low power listening protocols
    Uses a very long preamble to wakeup nodes
      Only works with very specific radios
  X-MAC: Uses short ‘probe’ packets to wakeup the receiver
    Probes contain the destination address  only receiver is woken up
    Probes can be acknowledged  less probes need to be sent
  LPL-MAC (TinyOS)
    Data packet are sent multiple times to wakeup the receiver
    CSMA/CA is used for each individual packet
  ContikiMAC (Contiki OS)
    Data packet are sent multiple times to wakeup the receiver
    Nodes try to learn when a node is awake (to minimise wakeup packets)
  …

## Slide 38: Low power listening MAC Protocols
Advantages
  Easy to implement
  Very robust: no synchronisation needed
  Can adapt to varying traffic requirements
Disadvantages
  All nodes are woken up regardless of the intended recipient
  Not suitable for:
    High network densities
    Networks with elevated bandwidth requirements
Depends on specific protocol & implementation

## Slide 39: Contention-based MAC Protocols
Many other MAC Protocols exist
  C-MAC, L-MAC, O-MAC, P-MAC, SCP-MAC, WiseMAC, Y-MAC, Z-MAC, …
Further reading:
  S-MAC: Ye, Wei, John Heidemann, and Deborah Estrin. "Medium access control with coordinated adaptive sleeping for wireless sensor networks." Networking, IEEE/ACM Transactions on 12.3 (2004): 493-506.
  T-MAC: Van Dam, Tijs, and Koen Langendoen. "An adaptive energy-efficient MAC protocol for wireless sensor networks." Proceedings of the 1st international conference on Embedded networked sensor systems. ACM, 2003.
  B-MAC: Polastre, Joseph, Jason Hill, and David Culler. "Versatile low power media access for wireless sensor networks." Proceedings of the 2nd international conference on Embedded networked sensor systems. ACM, 2004.
  X-MAC: Buettner, Michael, et al. "X-MAC: a short preamble MAC protocol for duty-cycled wireless sensor networks." Proceedings of the 4th international conference on Embedded networked sensor systems. ACM, 2006.

## Slide 40: MAC Protocols: IEEE 802.15.4
IEEE 802.15.4 (2006)
  The first ‘standard’ MAC Protocol for low-power wireless networks
  Nodes are organised into multiple Personal Area Networks (PAN)
  Two modes of operation
    Non-Beaconed Mode ≈ CSMA/CA
    Beaconed Mode: Channel is divided into superframes
      Controlled by a (PAN) controller
      Length of the active / sleep period is determined by the controller
      Contention Access Period: CSMA/CA
      Contention Free Period: TDMA slots allocated by the controller
Contention Access Period
Contention Free Period
Inactive period
Beacon
Beacon
Active Period
Sleep Period
Notes: Standardisation & adoption has been very slow:
-first standard quite complicated & only suited for infrastructured networks
 Partial implementations or replaced by different protocol entirely
-Now: standardisation is becoming more important, but standard has also grown
-eg: support for tdma-only operation (not previously available)
-also limited: TDMA frames defined, but not how slot allocation is to be performed
-infeasible to implement all of it
-not really an agreed upon ‘you MUST implement this’ subset
 Many incomplete & semi-compliant implementations remain

## Slide 41: MAC Protocols: IEEE 802.15.4
IEEE 802.15.4 (2015): TSCH
  Multi-Frequency TDMA (MF-TDMA) with frequency hopping
    TDMA slot-structure is expanded to multiple channels
    Each slot is identified by a slotId and a channel offset
    Frequency hopping: the TX-frequency changes every slot
      Pseudo-random hopping sequence
      slot-frequency is calculated from the slotId and the channel offset
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | …
0 | SS | SS |  | SS |  | SS |  | 
1 |  |  | EC |  |  |  |  | 
2 |  | DB |  |  |  |  |  | 
3 |  |  |  |  | BA |  |  | 
4 |  |  |  |  |  | CA |  | 
5 |  |  |  |  |  |  |  | 
slotId
channel offset
Notes: Other modes exist as well: only discuss TSCH here

## Slide 42: MAC Protocols: IEEE 802.15.4
IEEE 802.15.4 (2015): TSCH
  Two types of slots:
    Dedicated slots: only used for unicast traffic
    Shared slots: used mainly for sending beacons & broadcast traffic
      All nodes must listen to these slots
      Must have channel offset = 0
  Synchronization:
    Nodes transmit beacons during shared slots
    Nodes synchronize to:
      Beacons from other nodes ‘closer’ to the PAN coordinator
      Unicast data transmissions
    Internal clock is adjusted so average drift is minimized
  Note: IEEE 802.15.4 does not specify how unicast slots should be allocated

## Slide 43: IEEE 802.15.4: Frame format
PHY
MAC

## Slide 44: IEEE 802.15.4: Frame format
MAC Frame
  At most 127 bytes long (not including length byte)
  Designed for compression:
    Addressing: 16/64 bit
      Long addresses are (assumed to be) unique
      Short addresses are assigned by the PAN coordinator and are only valid within the PAN
    Four types of encryption each with it’s own overhead
    Only destination PAN ID is present if equal to source PAN ID
  MAC Overhead (data frames): 11 – 37 bytes
More Information: IEEE 802.15.4-2015
    http://standards.ieee.org/getieee802/download/802.15.4-2015.pdf

## Slide 45: Network Stack: Routing Layer

## Slide 46: Routing Protocols
Early protocols: borrowed from Ad-hoc networks
  Proactive protocols (OLSR, DSDV)
    Routes are advertised periodically in the network
    Each node maintains routes to all other nodes
  Reactive protocols (AODV, DyMO)
    Routes are discovered on-demand by flooding the network
    Nodes only maintain routes in which they are participating
AODV example:
A
C
B
D
E
NH(A)=A
NH(A)=C
NH(A)=A
NH(A)=D
NH(E)=E
NH(E)=D
NH(E)=C
RREQ dest=E
n. Hops=0
RREQ dest=E
n. Hops=1
RREQ dest=E
n. Hops=0
RREQ dest=E
n. Hops=2
RREQ dest=E
n. Hops=1
RREQ dest=E
n. Hops=1
RREQ dest=E
n. Hops=1
RREQ dest=E
n. Hops=2
RREQ dest=E
n. Hops=2
RREP
dest=A

## Slide 47: Routing Protocols
Shortcomings of MANET Protocols for sensor networks
  Proactive protocols
    Routing table size grows with the number of nodes in the network
      Not feasible for large scale sensor networks
    Route discovery & maintenance: uses periodic route advertisements
      Either too slow to react to changes or too bandwidth & energy consuming to even consider
  Reactive protocols
    Routing table
      Smaller than with proactive protocols
      Can still be quite large
    Flooding based route discovery
      All nodes are woken up each time a route is needed or updated
      Can cause severe congestion in dense networks
    Can detect & repair broken paths
      Route repair uses flooding
Notes: Flooding based issues example:
100+ node network
Imagine what would happen at network startup when all nodes try to establish a route to the sink node at the same time ?

## Slide 48: Routing Protocols
Some design challenges
  Scalability, Adapability, Fault tolerance, Connectivity, Coverage, …
  Find a good energy  route quality tradeoff
    Maintaining good routes is usually quite expensive
  Cope with different traffic patterns: Eg: event-based  periodic reporting
  Heterogeneity: nodes may have different capabilities
    Eg: more/less energy reserves, cpu, memory, …
    The routing protocol should exploit these differences if possible
  Data aggregation:
    Routes should be optimised to allow maximum agregation within the network
The exact challenges depend on
  The application requirements
  The network architecture
Notes: Important: stress that the challenges to overcome depend on the application !!
Eg: if no data agregation is possible, the routing protocol does not need to optimise for this

## Slide 49: Routing Protocols
Sensor network routing protocols
  Many different types & paradigms exist
Some examples:
  Hierarchical & Heterogeneity-based
    Different nodes perform different roles
    Eg: Clustering
  Location-based: exploit node locations to find routes
  Multipath-based
  Mobility-based
  Data-centric protocols
    Regard the network as a huge distributed data base
    Route ‘queries’ and ‘responses’ according to the contents of the message
Notes: Hierarchical goes hand in hand with heterogeneity. Example: clustering: divide the network into different clusters
All low-power sensor nodes connect to a high powered cluster head, inter-cluster comms done using for instance wifi
Multipath based: maintain multiple routes to the same destination
-redundancy: faster route repair when node fails
-even spreading of eneregy usage
Mobility based: optimise routing protocol for mobile nodes and ‘MOBILE SINKS’
-eg: instead of having expensive multihop forwarding, have a drone fly over the network twice a day to connect stats

## Slide 50: Routing Metrics
Which metric should be optimised when choosing routes ?
  Depends on the requirements of the application
  Two important types of metrics:
    Energy Usage
    End-to-End Reliability
  Some mathematical notations used
    : Energy cost of sending a packet from node i to node j
    : Reliability of link i ➞ j
    : routing path
    : route cost for sending a packet over link i ➞ j
    : route cost for sending a packet over routing path p
    : Remaining battery fraction of node i
Notes: Note: may other types of metrics exist besides energy usage & reliability, but these are generally regarded as the most important ones

## Slide 51: Routing Metrics
Hop Count:
  Tries to cover as much ‘distance’ as possible with each hop
    Selects very unreliable links
  Unusable for most types of wireless networks
Hop Count with blacklisting:
  Prune all links below a certain reliability threshold
  Links are guaranteed to have a certain minimum reliability
  Can easily cause network partition

## Slide 52: Reliability Metrics:
End-to-end reliability
  Ensures the best reliability possible
  No penalty for adding extra hops
    Has a tendency to result in very long paths
  Does not take asymmetric links into account
    Forward path will be different from the reverse path

## Slide 53: Reliability Metrics
Expected Transmission Count (ETX)
  “The expected number of PHY layer packets that need to be transmitted to send a single packet over the link”
  Trade-off between hop count & reliability
    Will generally use high quality links
    Lower quality links are used when needed
  Allows for asymmetric links
  Designed specifically for CSMA/CA
    May not work well with other MAC Protocols
Notes: Explain: etx considers both data & ack packets, if either gets lost the packet needs to be retransmitted
Also: etx expects the MAC protocol to be able to do retransmissions, and implicitly assumes that the MAC protocol will keep trying to send the packet until it is acknowledged. In reality this is not the case: the MAC protocol
Only tries to send the packet a limited number of times. This should be taken into account

## Slide 54: Estimating Link Reliability
Efficient routing requires the Link Reliability to be known
  Varies with distance between sender & receiver[1]
  Changes over time[1]
[1] Woo, Alec, Terence Tong, and David Culler. "Taming the underlying challenges of reliable multihop routing in sensor networks." Proceedings of the 1st international conference on Embedded networked sensor systems. ACM, 2003.

## Slide 55: Estimating Link Reliability
Can we use PHY Layer packet statistics ?
  RSSI & LQI provide an indication of the link quality
  Very noisy  Cannot be used directly for reliability calculations
Notes: Note that this does not mean that they are useless:
Flaws can be compensated for: eg: blacklisting bad links when they are detected

## Slide 56: Estimating Link Reliability
Probing
  Broadcast packets to measure the reliability directly
  Provides an estimate of the true reliability of the links
  Communication overhead can become quite large
    Link qualities vary over time  estimates must be adjusted
    Precision of the estimate increases with the number of packet sent
  Can be combined with other techniques to minimise overhead
Further reading:
  Woo, Alec, Terence Tong, and David Culler. "Taming the underlying challenges of reliable multihop routing in sensor networks." Proceedings of the 1st international conference on Embedded networked sensor systems. ACM, 2003.
  Gnawali, Omprakash, et al. "Interaction of retransmission, blacklisting, and routing metrics for reliability in sensor network routing." Sensor and Ad Hoc Communications and Networks, 2004. IEEE SECON 2004. 2004 First Annual IEEE Communications Society Conference on. IEEE, 2004.
  Woo, Alec, and David E. Culler. Evaluation of efficient link reliability estimators for low-power wireless networks. Computer Science Division, University of California, 2003.

## Slide 57: Energy Metrics:
Minimum Transmission Energy
  ,
  Minimizes the ‘global’ energy usage
  Does not take battery levels into account
    Nodes along the MTE-path die first
    Limited battery lifetime
Maximum-Minimum battery cost routing
  ,
  Minimizes traffic through nodes with minimal remaining energy
  Does not optimise overall energy usage of nodes with sufficient residual energy

## Slide 58: Energy Metrics:
Some more advanced metrics
  For all metrics:
  [1]
    Tuning parameter: λ
    Importance of energy cost increases exponentially with used energy
  [2]
    Tuning parameters: α, β
    Only considers energy cost of sender, not of the receiver
  Generalised version: [3]
    , : cost of sending & receiving over link i → j
C_{i,j}=e_{i,j}\left ( \lambda^{\left (1-E_{i}\right )} -1\right )
[1] https://www.cs.uni-paderborn.de/fileadmin/Informatik/AG-Karl/Lehre/SS12/Sensys/slides/sensys-ch11-id-centric-routing.pdf
[2] Shah, Rahul C., and Jan M. Rabaey. "Energy aware routing for low energy ad hoc sensor networks." Wireless Communications and Networking Conference, 2002. WCNC2002. 2002 IEEE. Vol. 1. IEEE, 2002.
[3] Chang, Jae-Hwan, and Leandros Tassiulas. "Maximum lifetime routing in wireless sensor networks." IEEE/ACM Transactions on Networking (TON) 12.4 (2004): 609-619.
C_{i,j}=\left (e_{i,j} \right)^{\alpha}\left (E_{i}\right )^{\beta}
C_{i,j}=\left (e_{i,j}^s \right)^{\alpha}\left (E_{i}\right )^{\beta} + \left (e_{i,j}^r \right)^{\alpha}\left (E_{j}\right )^{\beta}

## Slide 59: Routing Protocols
Further reading:
  Akkaya, Kemal, and Mohamed Younis. "A survey on routing protocols for wireless sensor networks." Ad hoc networks 3.3 (2005): 325-349.
  Singh, Shio Kumar, M. P. Singh, and D. K. Singh. "Routing protocols in wireless sensor networks–A survey." International Journal of Computer Science & Engineering Survey (IJCSES) Vol 1 (2010): 63-83.

## Slide 60: Routing Protocols: RPL
Observation: In sensor networks traffic flows mostly between the nodes and one or more ‘sink’ nodes connected to the backend.
RPL: IPv6 Routing Protocol for Low-Power and Lossy Networks (RFC 6550)
  First standardised routing protocol for low-power (sensor) networks
  Optimised for:
    Multipoint-to-point (mp2p): node-to-sink data reporting
    Point-to-multipoint (p2mp): directed queries, software updates, …
  Scalable & adaptable, low overhead
  Allows multiple routes to be maintained
    Different routes can be optimised for different objectives
  Decouples routing protocol from link selection strategy
  Extended encryption & authentication support
Notes: Mention it’s for IPv6 & that doing IPv6 stuff will be explained later

## Slide 61: RPL: DAGs & DoDAGs
RPL:
  Builds & maintains a Directed Acyclic Graph (DAG)
  Consists of multiple Destination Oriented DAGs (DoDAGs)
    DoDAG = DAG with single root (sink node)
    RPL operation is the same for each DoDAG
     we only consider a single DoDAG in the slides

## Slide 62: RPL: Node Rank
Each Node has a Rank within the DoDAG
  Rank ≈ Distance to root node
    Conceptually a fixed-point decimal number
    Only the integral part is used to compare node locations in the DoDAG
  Node A can only be a parent of Node B  DAGRank(A) < DAGRank(B)
    DAGRank(B) must be larger than the largest DAGRank in it’s parent set
    If two nodes have the same DAGRank, neither may be a parent of the other
      This is to avoid routing loops
R=2.3
R=1
R=2.9
R=3.2
R=4.1
R=5.1
Notes: Important: in the specs RANK is defined as a 16 bit integer and not a fixed-point decimal.
In all rank calculations howve r it is divided by a configurable constant (MinHopRankIncrease)
And the manner in which it is used is therefore conceptually the same as using a fixed point decimal

## Slide 63: RPL: Objective Functions
RPL uses an Objective Function (OF) to
  Calculate the Node Rank
  Decide which neighbors to use as parents
  This separates the route selection strategy from the operation of the routing protocol
Objective Functions
  Can make use of a wide range of node & link metrics
    RFC6551: Energy, Latency, Reliability, Throughput, …
    Others can be defined as needed
  Standardized OFs: RFC6552, RFC6997
    RPL also allows the OF to be built from scratch
  All nodes in the same DAG must use the same OF
Notes: Explain: the OF should also not be too ‘jittery’ in its calculations to keep routes stable

## Slide 64: RPL: DIO Messages
DoDAG Information Object (DIO)
  Contains:
    DoDAG configuration: DoDAG id, DoDAG seq.nr, OF, …
    Rank of the sending node
    Node & Path metric containers (to be used by the OF)
  Used by RPL to build & maintain the DoDAG
  Periodically broadcasted using a ‘Trickle Timer’ (RFC 6202)
    High TX rate during network setup & when inconsistencies are detected
      This includes configuration changes, node movement, …
    TX rate is gradually reduced as the network stabilises
  DIO messages are transmitted in an RPL ICMPv6 container
Notes: DIO == Similar to route advertisements in Proactive routing protocols

## Slide 65: RPL: DoDAG Construction
F
D
E
A
C
B
D
E
F
A
C
B
DIO
DoDAG Construction
  Root node joins DoDAG with Rank=1
  All DoDAG members periodically broadcast DIOs
  All Nodes maintain a neighbour list
    Based on received DIOs or other discovery techniques
  Objective Function
    Selects the parents from the neighbour list
    Sets the rank of the node
  After joining the node starts broadcasting DIOs
  The root can initiate a new DoDAG by increasing the DoDAG Seq.Nr
 | A | B | C | D | E | F
Neighbours | B,C | A,D,E | A,D,E | B,C,F | B,C,F | D,E
Parents |  | A | A | B,C | C | D,E
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 5.1
 | A | B | C | D | E | F
Neighbours |  | A | A |  |  | 
Parents |  |  |  |  |  | 
Rank | 1 |  |  |  |  | 
 | A | B | C | D | E | F
Neighbours |  | A | A |  |  | 
Parents |  | A | A |  |  | 
Rank | 1 | 2.3 | 2.9 |  |  | 
 | A | B | C | D | E | F
Neighbours | B,C | A | A | B,C | B,C | 
Parents |  | A | A |  |  | 
Rank | 1 | 2.3 | 2.9 |  |  | 
 | A | B | C | D | E | F
Neighbours | B,C | A | A | B,C | B,C | 
Parents |  | A | A | B,C | C | 
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 
 | A | B | C | D | E | F
Neighbours | B,C | A,D,E | A,D,E | B,C | B,C | D,E
Parents |  | A | A | B,C | C | D,E
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 5.1
DIO
DIO
DIO
DIO
DIO
DIO
DIO
DIO
DIO
DIO
DIO
DIO
DIO

## Slide 66: RPL: Node Movement
A
Nodes can move in the DoDAG over time
  Node can increase/decrease their rank
Moving Up: decreasing rank
  Eg: when a shorter path to the root is discovered
  Rank/Parent rules still apply
    Rank can only be decreased after old parents are removed from the parent set
 | A | B | C | D | E | F
Neighbours | B,C | A,D,E | A,D,E | B,C | B,C | D,E
Parents |  | A | A | B,C | C | D,E
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 5.1
D
E
F
C
B
DIO
DIO
DIO
 | A | B | C | D | E | F
Neighbours | B,C,F | A,D,E | A,D,E | B,C | B,C | A,D,E
Parents |  | A | A | B,C | C | D,E
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 5.1
 | A | B | C | D | E | F
Neighbours | B,C,F | A,D,E | A,D,E | B,C | B,C | A,D,E
Parents |  | A | A | B,C | C | A
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 2.3

## Slide 67: RPL: Node Movement
A
Moving Down: increasing rank
  Eg: when node loses connection to parents
  Nodes must ‘poison their routes’ before doing so
    Broadcast DIO with RANK=∞
    This reduces the chance of creating a routing loop
  Nodes may never increase their rank beyond ‘LeastAdvertisedRank’+’MaxRankIncrease’
    This prevents a count-to-infinity scenario when multiple nodes increase their rank
 | A | B | C | D | E | F
Neighbours | B,C | A,D,E | A,D,E | B,C | B,C | D,E
Parents |  | A | A | B,C | C | D,E
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 5.1
D
E
F
C
B
 | A | B | C | D | E | F
Neighbours | B,C | A,D,E | A,D,E | B,C | B,C | D,E
Parents |  | A | A | B,C | C | A
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 2.3
 | A | B | C | D | E | F
Neighbours | B,C,F | A,D,E | A,D,E | B,C | B,C | A,D,E
Parents |  | A | A | B,C | C | A
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 2.3
DIO
DIO
 | A | B | C | D | E | F
Neighbours | B,C | A,D,E | A,D,E | B,C | B,C | D,E
Parents |  | A | A | B,C | C | D,E
Rank | 1 | 2.3 | 2.9 | 4.1 | 3.2 | 5.1
Notes: Explain: route poisoning does not prevent loop creation since the DIO messages may get lost.
RPL detects & breaks routing loops when data is sent over them

## Slide 68: RPL: Downward routes
A
D
E
F
C
B
DAO
DoDAG creation:
  builds upward routes only
Downward routes
  Created by unicasting ‘DAO’s to the root
    DAO=Destination Advertisement object
    Similar to RREPs in AODV
  Usually transmitted through the ‘preferred parent’ only
  Only for nodes requiring a downward route

## Slide 69: RPL: Downward routes
A
D
E
F
C
B
Downward routes
  Non-Storing Mode:
    Only the root maintains a downward routing table
    Packets are forwarded downwards using source routing
    Inter-node transmissions always pass over the root
  Storing Mode:
    All nodes maintain a downward routing table
    Packets are forwarded hop-by-hop
    Inter-node transmissions only pass over the nearest common ancestor`
DATA
DATA

## Slide 70: RPL: Additional Features
Additional Features of RPL
  Loop detection:
    RPL does not guarantee loop-free routing paths
    Loops are detected & resolved when data is sent over them
  Multiple Downward Paths:
    Slides only show example for single downward path per destination
    RPL supports multiple downward paths per destination
Full specifications:
  RFC 6202: Trickle Timer
  RFC 6550: RPL operation
  RFC 6551: Standardised Routing Metrics
  RFC 6552, RFC 6997: Standardised Objective Functions

## Slide 71: 6LowPAN

## Slide 72: The Internet of Things
Sensor network evolution
Special Purpose &
Research Networks
Commercial Automation Solutions
[1]
[2]
[2]
[1] http://www.cs.berkeley.edu/~binetude/ggb/
[2] http://siliconangle.com/blog/2013/06/04/2013-the-year-of-the-internet-of-things/
Notes: Sensor networks have come a long way: Not only ‘custom built special purpose’ networks:
integration & interoperability become more important
Goal: Internet Of things: basically attach every sensor directly to the internet

## Slide 73: The Internet of Things
Sensor network evolution
  Existing requirements continue to exist
  Interoperability ?
  Interconnectivity ?
  Ease of use ?
Internet of Things: Connect everything to the internet
  Goal: end-to-end TCP/IP connectivity with smart devices
    Industrial control systems, Smart Roads, …
    Home automation:
      TV, Lights, Heating, Smart metering, ..
      Smart appliances: fridge, washing machine, ...
      Smart clothes, food, …
  Applies to sensor networks as well

## Slide 74: 6 LowPAN
IP in Sensor Networks
  IPv4 = deprecated  Use IPv6 instead
IPv6  IEEE 802.15.4
  IEEE 802.15.4: max 127 byte frames
  IPv6
    Requires MAC-Layer to support 1280-byte packets
    IPv6 Header is at least 40 bytes long
      At least 48% overhead from IPv6 & UDP alone !!!
6LowPAN
UDP
MAC
IPv6 Header
DATA
23B
40B
8B
Max 53B
2B (FCS)

## Slide 75: 6LowPAN
6LowPAN: IPv6 over Low powered (personal) area networks
  Adaptation layer between IEEE 802.15.4 and IPv6
  Defined by IETF Standards
    RFC4944, RFC6282, RFC6775
  Stateless & Stateful IPv6 Header compression
  Fragmentation
  Low-power alternative to IPv6 Neighbour Discovery
  End-to-end Internet integration
IPv6
[1] Shelby, Zach, and Carsten Bormann. 6LoWPAN: The wireless embedded Internet. Vol. 43. Wiley. com, 2011.
[1]
Notes: Remember: main goal of 6LowPan: reduce header size

## Slide 76: 6LowPAN
Protocol Stack
Ethernet PHY
Ethernet MAC
IPv4
TCP
UDP
ICMP
IEEE 802.15.4 PHY
IEEE 802.15.4 MAC
IPv6
UDP
ICMP
6LowPAN
Physical
Data Link
Network
Transport
HTTP, VoIP, …
CoAP, …
Application
TCP/IP Protocol stack
IPv6
6LowPAN Protocol stack
Notes: Note: CoAP == Webservices for Sensor networks

## Slide 77: 6LowPAN
Architecture
  6LowPAN = ‘stub’ network
    Standalone network with one or more internet uplinks
    Does not route data for other networks
    Each 6LowPAN network corresponds to an IEEE 802.15.4 PAN
[1] Shelby, Zach, and Carsten Bormann. 6LoWPAN: The wireless embedded Internet. Vol. 43. Wiley. com, 2011.
[1]
Notes: Stub network example: basically every home network in the world

## Slide 78: 6LowPAN
Two operating modes
  Meshing Under
    All nodes are on the same IPv6 link
    6LowPAN handles meshing & multihop broadcasting
  Routing Over
    IPv6 links correspond to the underlying links
    Routing & multicast are handled in IPv6
MAC
IPv6
6LowPAN
UDP
MAC
IPv6
6LowPAN
UDP
MAC
IPv6
6LowPAN
MAC
IPv6
6LowPAN

## Slide 79: 6LowPAN: Frame format
General Frame Structure
  Stacked headers prefixed with dispatch byte
    Identifies the header type
    May contain header information
…
MAC
DATA
H1
D
P
H2
HN
D
P
D
P
Pattern Header Type
+------------+------------------------------------------------+
| 00 xxxxxx | NALP - Not a LoWPAN frame |
| 01 000000 | ESC - Additional Dispatch byte follows |
| 01 000001 | IPv6 - Uncompressed IPv6 Addresses |
| 01 000010 | LOWPAN_HC1 - LOWPAN_HC1 compressed IPv6 |
| 01 000011 | reserved - Reserved for future use |
| ... | reserved - Reserved for future use |
| 01 001111 | reserved - Reserved for future use |
| 01 010000 | LOWPAN_BC0 - LOWPAN_BC0 broadcast |
| 01 010001 | reserved - Reserved for future use |
| ... | reserved - Reserved for future use |
| 01 111110 | reserved - Reserved for future use |
| 01 1xxxxx | LOWPAN_IPHC - LOWPAN_IPHC compressed IPv6 |
| 10 xxxxxx | MESH - Mesh Header |
| 11 000xxx | FRAG1 - Fragmentation Header (first) |
| 11 001000 | reserved - Reserved for future use |
| ... | reserved - Reserved for future use |
| 11 011111 | reserved - Reserved for future use |
| 11 100xxx | FRAGN - Fragmentation Header (subsequent)|
| 11 101000 | reserved - Reserved for future use |
| ... | reserved - Reserved for future use |
| 11 111111 | reserved - Reserved for future use |
+------------+------------------------------------------------+
Figure 2 from RFC 4944, updated with new information from RFC 6282
Deprecated
Replacement
Value has changed since original specification
Notes: Remember: main goal of 6LowPan: reduce header size

## Slide 80: 6LowPAN: Frame format
Mesh Header
  Used to ‘mesh under’ an IPv6 link
  Uses 16/64-bit IEEE 802.15.4 addresses
    V/F bits: indicate whether short or extended addresses are used
    Previous & Next hop information retrieved from MAC Header
Broadcast Header
  Used for ‘mesh under’ multihop broadcasting
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 0|V|F|HopsLft| originator address, final address
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0|1|LOWPAN_BC0 |Sequence Number|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Notes: Note: first 8 bits are the Dispatch byte

## Slide 81: 6LowPAN: Frame format
Fragmentation headers
  First fragment:
  Next fragments:
  Used when an IPv6 packet does not fit in a single MAC frame
    Datagram tag: identifies all fragments of the same packet
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 0 0 0| datagram_size | datagram_tag |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 1 0 0| datagram_size | datagram_tag |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|datagram_offset|
+-+-+-+-+-+-+-+-+

## Slide 82: 6LowPAN: IPv6 Header compression
Payload
Version
Traffic Class
Flow Label
Payload Length
Next Header
Hop Limit
Source Address
Destination Address
Source Port
Destination Port
UDP Length
Checksum
Full IPv6/UDP Headers: 48 Bytes
Dispatch + Lowpan_IPHC
Lowpan_NHC
SP
DP
Checksum
Payload
Minimal LowPAN Headers: 6 Bytes
Notes: Remember: main goal of 6LowPan: reduce header size

## Slide 83: 6LowPAN: IPv6 Header compression
Compression techniques
  Strip out non-essential fields:
    Traffic Class, Flow label, Hop limit, …
    header / payload lengths: can be calculated from packets size
  Reduce size of other fields:
    IPv6 address fields: can be compresses or removed altogether
      64-bit prefix: same for all nodes in the network  not needed
      64-bit device-id: can be calculated from the MAC-address
    UDP source / destination ports: can be reduced to 4 bits each
    Next header field: can be reduced to a few bits
Compression can be enabled/disabled/configured for each field individually

## Slide 84: 6LowPAN: IPv6 Header compression
Base Header
+-------------------------------------+------------------------
| Dispatch + LOWPAN_IPHC (2-3 octets) | Compressed IPv6 Header
+-------------------------------------+------------------------
LOWPAN_IPHC Encoding
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
| 0 | 1 | 1 | TF |NH | HLIM |CID|SAC| SAM | M |DAC| DAM |
+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+---+
TF = Traffic Class, Flow Label
NH = Next Header Flag
HLIM = Hop Limit
CID = Context Identifier Extension
SAC = Source Address Compression
SAM = Source Address Mode
M = Multicast Compression
DAC = Destination Address Compression
DAM = Destination Address Mode
Shelby, Zach, and Carsten Bormann. LoWPAN: The wireless embedded Internet. Vol. 43. Wiley. com, 2011.
Notes: The short explanation:
-LowPAN_IPHC specifies fields present + type of compression, compressed fields placed after IPHC
-Traffic class + flowid : 3 different compression modes or not present
-Next Header: specifies if next header is also compressed (not -> normal IPv6 from now on)
-Hop limit: either 1, 64, 255 or specified in separate byte
-Remainder: source & destination addessing

## Slide 85: 6LowPAN: IPv6 Header compression
IPv6 Address compression
  IPv6 Address:
  Prefix compression:
    None: full prefix is present
    Stateless: assume link-local prefix
    Statefull: predefined prefix
      Specified by a 4-bit Context Identifier
  Interface ID representation
    64-bit: full Interface ID is stored in the packet
    16-bit: only the 16 least significant bits are stored
      Other bits are either a fixed prefix or known through the Context Identifier
    None: IEEE 802.15.4 address is used as Interface ID
      Retrieved from MAC or LowPAN meshing header
64-Bit Prefix
64-Bit Interface ID

## Slide 86: 6LowPAN: IPv6 Header compression
LowPAN_NHC: Next-header compression
  Compression format for popular headers
IPv6 Extension Headers:
    EID: identifies the header type:
      Hop-by-hop, routing, fragmentation, …
    NH: whether or not the next header is compressed
+----------------+---------------------------
| var-len NHC ID | compressed next header...
+----------------+---------------------------
0 1 2 3 4 5 6 7
+---+---+---+---+---+---+---+---+
| 1 | 1 | 1 | 0 | EID |NH |
+---+---+---+---+---+---+---+---+

## Slide 87: 6LowPAN: IPv6 Header compression
UDP Header compression:
  Conforms to LOWPAN_NHC
  Checksum can be removed under certain circumstances
  Port Compression:
    Source & Destination ports can be compressed to 4 bits each
    Stateless compression, no context information
0 1 2 3 4 5 6 7
+---+---+---+---+---+---+---+---+
| 1 | 1 | 1 | 1 | 0 | C | P |
+---+---+---+---+---+---+---+---+

## Slide 88: 6LowPAN: Neighbour Discovery
RFC 4861: Neighbour Discovery for IPv6
  Used for ‘Bootstrapping’ IPv6 nodes
    Node broadcasts ‘Router Solicitation’
    Router answers with ‘Route Advertisement’
      Contains IPv6 Prefix & Route information
    Node chooses IPv6 address based on prefix info & Interface ID
    Node broadcasts ‘Neighbour Solicitation’ with chosen address
      No reply  safe to use address
H
H
H
H
R
R.Adv
R.Soll
R.Soll
R.Soll
R.Soll
N.Soll
N.Soll
N.Soll
N.Soll
H

## Slide 89: 6LowPAN: Neighbour Discovery
RFC 4861: Neighbour Discovery for IPv6
  Used for ‘Bootstrapping’ IPv6 nodes
  Used for L3L2 address resolution
    Node broadcasts ‘Neighbour Sollicitation’
      Contains the IPv6 address to be resolved
    Owner of the IPv6 address replies with ‘Neighbour Advertisment’
      Contains L2 address corresponding to the IPv6 address
H
H
H
H
R
N.Soll
N.Soll
N.Soll
N.Soll
N.Adv

## Slide 90: 6LowPAN: Neighbour Discovery
Can we use RFC 4861 in LowPANs ?
  IPv6 link-local multicast = LowPAN wide broadcast
    Network is flooded each time
      A Router Solliciation is sent
      A L3  L2 address translation is performed
  Node movement within the LowPAN triggers address reconfiguration
  RFC4861 has no support for statefull address compression
RFC 6775: Neighbour Discovery for 6LowPANs
Notes: Note1: IPv6 Broadcasts are translated into LowPAN wide multihop broadcasts

## Slide 91: 6LowPAN: Neighbour Discovery
Network Structure:
  Route-Over:
    6LBR: 6LowPAN Border Router
      Connects the LowPAN to the outside world
      Responsible for prefix propagation in the LowPAN
    6LR: 6LowPAN Router
      Forwards IPv6 Packets within the LowPAN
      Aids in Multihop Neighbour Discovery
    6LN: 6LowPAN Node
      End nodes in the LowPAN
  Mesh-Under: no 6LR’s present
    Entire LowPAN is treated as a single IPv6 Link
6LBR
6LR
6LR
6LR
6LN
6LN
6LN
6LN
6LN

## Slide 92: 6LowPAN:
Modifications to Neighbour Discovery messages
  6CO: 6LowPAN Context Option
    New option for Route Advertisements
    Contains statefull address compression context information
  ARO: Address Registration option
    New option for Neighbour Sollicitations
    Allows 6LH’s to register their addresses with a 6LR
  ABRO: Authorative Border Router Option
    IPv6 Option for Route Advertisements
    Used to announce the 6LBR in the LowPAN
  Full list: see RFC 6775

## Slide 93: 6LowPAN: Neighbour Discovery
Bootstrapping
  6LN broadcasts router sollicitation
  6LRs in reach reply with router advertisement
    Contains ABRO, 6CO & prefix information
  6LN Registers its addresses with one or more 6LRs
    Unicasts ‘Neighbour Solicitation’ containing ARO
  6LR asks 6LBR if the IPv6 address is already in use
  6LBR replies to 6LR
  6LR Sends ‘Neighbour Advertisement’ to 6LH
    Contains ARO: status indicates registration success/failure
  The 6LN may now start acting as a 6LR to other nodes
Note: 64 bit MAC addresses are assumed to be unique
  6LBR check is skipped for 64-bit MAC addresses
6LBR
6LR
6LR
6LR
6LN
6LN
6LN
R.Soll
R.Soll
R.Adv
N.Soll
DAR
DAC
N.Adv
6LR

## Slide 94: 6LowPAN: Neighbour Discovery
L3  L2 Address resolution
  Each 6LH learns the L2 addresses of its 6LRs through the registration process
  6LRs register their addresses with their 6LR neighbours
    This is done in exactly the same manner as 6LH address registration
Further Reading
  RFC4944: The original 6LowPAN specification
  RFC6282: Revisions to the 6LowPAN specification
  RFC6775: Neighbour Discovery for 6LowPANs

## Slide 95: Sensor network platforms

## Slide 96: Typical sensor nodes
MicaZ
4K RAM 128K Flash
UCMote ProtonB
16K RAM 128K Flash
AVR Raven
16K RAM 128K Flash
Tmote SKY
10K RAM
48K Flash
Zolertia Z1
8K RAM
96K Flash
Zolertia Re-Mote
32K RAM
512K Flash
Notes: -Some examples of sensor nodes
(shown from old->new)
-limited in capabilities even for recent ones
-originally: needed to save power, still the case
-secondly: cost cheaper components -> lower price per node -> in this case: higher profit

## Slide 97: Operating Systems
Challenges for the sensor network OS:
  Code & memory space
  Nodes are often custom-built, special-purpose hardware
     no OS will work ‘out of the box’
  Missing hardware features:
    Memory Management Unit (MMU)
    Protected access mode
  Device drivers
    Applications often require low level access to devices
 Not uncommon NOT to use an OS at all
Notes: Problems for os:
space: try fitting the linux kernel in 10k ram…
hardware is special purpose  even if you have an os: requires tweaking / hacking to get it working on your platform
not all features required by an OS are present most prominent
-MMU (if you have this, you are probably running linux)
-protected access mode
device drivers: ideally: shielded from application but try implementing TDMA with micro-second accuracy without low-level access to the devices
Not uncommon for an application NOT to use an OS at all (depending on the specific application)
  If you have specialised hardware that only needs to perform a single function and you’re the only one who is going to use it: why bother with an OS ?
Do you have to start from scratch every time: no
  Quite a number of Osses exist but they are quite different from a traditional OS

## Slide 98: Operating Systems
Sensor node OS: More framework than OS
  Provides OS-like features but end-control lies with the application itself.
  Does not have the capabilities of a ‘traditional OS’
    Memory protection ? NO
    Dynamic memory allocation ? Maybe
      No MMU, no paging  extremely limited
    Multithreading ? Maybe
      Some provide it, others offer task scheduling
OS handles most of the dirty details but:
  In the end the application can do whatever it wants
  Offers no protection against screwups
Notes: Do you have to start from scratch every time: no
  Quite a number of Osses exist but they are quite different from a traditional OS
Osses: do not provide everything you would expect
  Best way to look at it: a framework that includes some of the things you would expect an OS to do into your application image
  Single image built from a collection of application code & libraries
  Dynamic memory: some do, some don’t: remember no virtual memory,  all the issues solved with paging / virtual memory come back into play again (fragmentation, …)
    not available / not used most of the time
  Multi-process support: none single-application --> shouldn’t be necessary
    No memory protection: no MMU
    Multithreading: some provide it some don’t
      Alternative: task scheduling within a single thread
  Scheduling:
Helps you, but won’t prevent you from messing up
  Eg: 0x0 is considered to be a valid pointer address
  Want to write outside your allocated memory ? : go right ahead
  Busy loop -> hangs the entire node, but go right ahead
Debugging: very limited capabilities: usually nothing more than some leds & printf
  Stepping / tracing requires specialized HW, shuts down the entire MCU, not only the piece of code you are looking at
  Dynamic module loading??

## Slide 99: Operating systems
TinyOS
  The first sensor network OS
  Basic OS Features:
    Non-preemptive Task scheduler & Timers
    No dynamic memory
    No real-time support
  nesC language: modular version of C designed for extreme reusability
  Geared at sensor network prototyping & research
    Suitable for extremely low-power devices
    Fully fledged but non standard-compliant network stack:
      CSMA/CA or LPL-MAC, 6LowPAN & CoAP
  Still used but not as actively maintained as it used to be
Further reading: http://www.tinyos.net

## Slide 100: Operating Systems
Contiki-OS
  Wider range of OS Features
    Scheduling:
      Protothreads: threads without a stack
      Non-preemptive multithreading (limited support)
    Limited dynamic memory support
      Allocation within statically defined buffer
      malloc(): only for a few specific platforms
    Dynamic module loading: Best considered as ‘Experimental’
    Basic filesystem & multi-application support
  Most ‘advanced’ features are only available on a few specific platforms
Notes: Note: contiki has the habbit of implementing features half-heartedly for one or two platforms and than flatly saying that they support it  keep your eyes open

## Slide 101: Operating Systems
Contiki-NG: “Contiki for the next generation of IoT devices”
  Fork of original Contiki-OS code
  Basic principles are the same but not backwards compatible
  Drops support for “ancient” sensor platforms
  Drops support for outdated network stacks
  Adds support for newer sensor platforms (e.g. Zolertia Re-Mote)
  Add support for IEEE 802.15.4 TSCH
  You’ll be using Contiki-NG in this course
Notes: Note: Contiki-OS has three separate network stacks…

## Slide 102: Contiki
Protothreads:
  Conceptually: ‘Stateless threads’
    Execution stack is only available while the thread is running
    When the thread is paused, only the program-counter is preserved
  Non-preemptive:
    State is lost on context switch
      thread itself decides when this occurs
    Thread only pauses while waiting for an event to occur

## Slide 103: Contiki: Protothreads example
#include "pt.h"
PT_THREAD(sender(struct pt *pt))
{
PT_BEGIN(pt);
while(keep_running) {
PT_WAIT_UNTIL(pt,
key_pressed());
send_packet();
timer_set(&timer, TIMEOUT);
PT_WAIT_UNTIL(pt,
timer_expired(&timer));
}
PT_END(pt);
}
#include "pt.h"
char sender(struct pt *pt)
{
switch(pt->lc)
{
case 0:
while(keep_running) {
pt->lc = 7;
case 7:
if(!key_pressed())
return 0;
send_packet();
timer_set(&timer, TIMEOUT);
pt->lc = 10;
case 10:
if(!timer_expired(&timer))
return 0;
}
}
pt->lc = 0
return 3;
}
Notes: -Show left code first: explain what conceptually everything does
-PT_THREAD: Declare a new thread
-PT_BEGIN: thread execution starts here, place nothing in front of it for reasons that will become aparent very shortly
-PT_WAIT_UNTIL: wait until a specific condition is true, other commands for suspending execution also exist
-PT_END: thread execution stops here
-Finished thread may be rescheduled once completed
How did they do this: ? This is pure C-code  Macro magic
-Show on right side what the code translates to
- is code directly from gcc, with a few unnecessary statements removed && with some code cleanup added
-Highligt macro expansion: show original code is still there
-Hide it & explain:
-Each PT_THREAD == function that is called by the task scheduler whenever it needs to do something
-Makes use of extremely dirty trick in C: select statement does NOT what we would expect it to do:
-Select is not something that executes a block of code based on a value
-it jumps to a specific line in a block of code based on a value
-may contain if’s while, for’s, … select is very similar to GOTO’s
-PT_BEGIN: start switch statement: ptlc represents the Program counter: eg: where we are in the thread
-whenever we yield: store the current position by adding a ‘case’ statement, storing the value & returning
-next time function is invoked: ‘thread’ continues where it left off

## Slide 104: Contiki
Protothreads
  From the programmer’s point of view: lightweight thread
    Code structure mimics that of thread-based programming
  From the scheduler’s point of view: tasks
    Each ‘protothread’ is a task to be repeatedly scheduled for execution
  Drawbacks
    No state:
      local variables are cleared when the thread yields
       use static variables if the value needs to survive a ‘yield’
    Thread can only be yielded at the top-most level
      Functions called from the protothread cannot yield the thread
    Waiting for an event may prevent the CPU from entering sleep-mode
      The protothread is rescheduled until the event has occurred

## Slide 105: Contiki-NG Network stack
Monolithic Network stack
  Some choice in components
  Difficult to add new ones
Network Layer
  6LowPAN + IPv6 + RPL
    6LowPAN
      Adaptation layer
      Compresses / extracts packets on-the-fly
    RPL: routing protocol
      Partial implementation
        RPL spec. is very big
MAC Layer
  Choice of either TSCH or CSMA/CA
MAC Layer
uIPv6
Application
TCP
UDP
ICMPv6
IPv6
HTTP
CoAP
…
6LowPAN
RPL
TSCH
CSMA/CA

## Slide 106: Contiki
CooJa: Contiki Network Simulator
  Event-based simulator
  Sensor node VM
    Emulates device hardware
    Interprets sensor node byte-code directly
    Image in VM == Image on device
  Powerfull debugging & research tool
Further Reading
  http://contiki-ng.org/
  https://github.com/contiki-ng/contiki-ng/wiki
  Contiki-NG source code:
    https://github.com/contiki-ng/contiki-ng
Notes: Event based  all event which can occur: sending of a packet, timer being fired button being pressed: all processed individually
-all events stored in order in an event queue, processed in order across the entire network
-simulated time != real time: may be faster / slower depending on #nodes, #events
-main advantage: does not depend on host timer --> adding more nodes slows the sim down, but does not invalidate the results
Sensor node VM
-interprets compiled code just like eg Java VM interprets java byte code
-image in vm same as one deployed on the device  very little differences between VM & real behavior  extremely powerful debugging tool even for mu

## Slide 107: Operating Systems
Riot-OS
  Internet-of-Things-OS:
    Develop on PC, deploy on sensor node
    Supports both C & C++
  Supports multithreading & dynamic memory
  http://www.riot-os.net
FreeRTOS: Free Real-Time OS
  Designed for commercial usage
    Multithreading & Dynamic memory
    Priority Thread scheduler
    E. Usage often less of a concern
  MCU’s are usually a bit more powerful
  http://www.freertos.org
Notes: RiOT OS: Nice idea, but not really meeting its goals yet (eg STL not fully supported)
FreeRTOS: along for quite a while
-focus on commerial embedded development
-eg: MCU in oven, washing machine, …
-other priorities:
-starting point for product development
-learning curve ?, easy to use: ?
-not uncommon to hack around with makefiles & write some own headers

## Slide 108: What will you do?

## Slide 109: What will you do?
You will research TSCH sensor networks
  Using 6TiSCH “minimal configuration” stack: TSCH, 6top sublayer, RPL
  Using Contiki-NG
  Using the Zolertia RE-Mote (868 MHz & 2.4 Ghz)
You will answer different research questions throughout the year
  What is the effect of parameter X on metric Y?
  Which (set of) parameters performs best in terms of metric X?
  How can you improve metric X?
  …

## Slide 110: What will you do?
You will write your results down in a scientific paper
  Paper should be at least 5 pages 2-column IEEE style
  Template available on blackboard
  A conference-ready paper containing:
    What you investigated
    A description of your test setup
      Explain not only the how but also the why
    Your results + explanation

## Slide 111: Practical organisation
Contact information:
  Glenn Daneels: glenn.daneels@uantwerpen.be
  Carmen Delgado: carmen.delgado@uantwerpen.be
Teams of two/three people
  Same team ≈ same grade
  Report problems immediately
    We hear nothing = everything is ok
  Submit your groups by e-mail by the end of the week
    Send your e-mail to: glenn.daneels@uantwerpen.be

## Slide 112: Practical organisation
If problems arise with the software or hardware
  Look in the documentation & source code
  Ask Google
  Send us an e-mail (glenn.daneels@uantwerpen.be)
    Don’t wait until it’s too late
If problems arise your partner(s)
  Contact us ASAP
  We hear nothing = all went well

## Slide 113: Timing
Project starts now
  Throughout the year you will get different research questions
Deadline final paper
  The day before the Christmas holiday
During exam period
  Presentation on results

## Slide 114: What is your first assignment?
Obligatory reads:
  Vilajosana, Xavier, et al. "IETF 6TiSCH: A Tutorial." IEEE Communications Surveys & Tutorials (2019).
  Duquennoy, Simon, et al. ”TSCH and 6TiSCH for Contiki: Challenges, design and evaluation." 2017 13th International Conference on Distributed Computing in Sensor Systems (DCOSS). IEEE, 2017.
  Papers are available on Blackboard
   You want to learn more? See http://scholar.google.be and look for keywords such TSCH, 6TiSCH, RPL, Contiki, 6top, etc.

## Slide 115: What is your first assignment?
Get to know the firmware:
  https://github.com/contiki-ng
  Obligatory: Set up Contiki-NG on your system:
    https://github.com/contiki-ng/contiki-ng/wiki#setting-up-contiki-ng
Get to know the hardware:
  https://github.com/contiki-ng/contiki-ng/wiki/Platform-zoul
Obligatory: Get the “Hello, World!” Example running
  https://github.com/contiki-ng/contiki-ng/wiki/Tutorial:-Hello,-World!
  Make sure that you get it running as a native node at the very least
  Also try to run it on the Zolertia nodes
    Not a problem if it doesn’t work yet

## Slide 116: First meeting
We will have a first meeting where you will show your progress and ask your questions:
  At “The Beacon” campus (Sint-Pietersvliet 7, 2000 Antwerpen)
  Bring your sensors and laptops
  Select the slots you are available by the end of the week (13/10): https://doodle.com/poll/smmr8tdnm2hfunr6

## Slide 117: Questions ?